## Slide 1: Bioimage Analysis in Fiji
https://image-analysis-workshop.github.io
James Crichton
Experimental Officer (Imaging and Image Analysis)
@TheRILD

## Slide 2: Outline
Slides + Fiji Exercises detailed on website
What is an image?
Image processing, making figures
Recording processes and starting to code
Calculating quantitative measurements

## Slide 3: Images are arrays of values

## Slide 4: Bit Depth
Image values exist in a range referred to as the “bit depth”
Numbers fundamentally are binary (0 or 1)
  1bit = 21 i.e. 2 values
  8bit = 28 i.e. 256 values
  16bit = 216 i.e. 65536
  Etc

## Slide 5: How are values generated?
Pete Bankhead – Introduction to Bioimage Analysis

## Slide 6: Factors affecting pixel values
Time spent detecting photons (exposure time)
  Longer exposures result in higher values
Numerical aperture
  Higher NA can collect more photons, resulting in higher values
Detector sensitivity (gain)
  Higher sensitivity increases detection of photons
  (Also increases detection of noise)
Pixel values are rarely meaningful in isolation.
Need to compare between images and capture with identical parameters.

## Slide 7: Image histogram
Image values presented as frequencies
Here, 0 is white and 255 is black

## Slide 8: Dynamic Range
The difference between the highest and lowest recorded values in an image
To maximise the potential of a microscope and build the most informative dataset
Optimise by considering how you set your capture parameters
  Short exposure: low dynamic range. Little info on intensity variation in samples
  Long exposure: risk of over saturating image and losing linear relationship between values
Max Value

## Slide 9: Lookup tables (LUTs)
Fluorescence images have no inherent colour (greyscale)
Visualise the values using different pallets (doesn’t change the values)

## Slide 10: Adjusting Appearance
Adjust appearance only
Adjust appearance and values by Applying (“clipping”)

## Slide 11: Images can look identical but contain different values
Pete Bankhead – Introduction to Bioimage Analysis

## Slide 12: Images can look vary different a contain the same values
Pete Bankhead – Introduction to Bioimage Analysis

## Slide 13: Other Image Types
RGB Images
RGB images are inherently coloured
3 values per pixel (red, green, blue)
Multi-dimensional images
Multiple greyscale images stacked together
  Channels (multiple stains)
  Z-position (3D)
  Time (time-series)
  Location (multi-point)

## Slide 14: Metadata
Information relating to an image, saved behind the scenes
Typically very detailed
When was it taken
Microscope used
Filters
Exposures
Other capture settings
Objective
Image scale (px/um)
Bits of this exhaustive list of information can be very useful.
Always preserve a raw copy of your images with this data.

## Slide 15: Page 1 Exercises

## Slide 16: 3D Images
3D images can be useful for analysis but less convenient for visualising
Take a slice
Project signal:
  E.g. Maximum intensity projection (MIP)
Different methods depending on what you want to show
Z-stack
Chosen Slice
Max Intensity Projection

## Slide 17: Scale Bars
Essential for publication
Necessary for calibrating any measurements
Scale of image is the relationship between pixels and real distance (e.g. μm)
Determined by camera and the objective lens used
Scale is typically recorded in the image metadata

## Slide 18: Showing Merged and Separated Channels
It’s often to show merged and separate channels
Consider your choice of lookup tables carefully
https://www.ascb.org/science-news/how-to-make-scientific-figures-accessible-to-readers-with-color-blindness/

## Slide 19: The ROI Manager
Enables you to record coordinates of regions of interest for reference and reuse
This tool is also very valuable in analysis

## Slide 20: Interpolation when rotating
Think about what rotations are doing to your image data!

## Slide 21: Exercises Page 2

## Slide 22: The Recorder
Records actions and displays code to repeat them
Great way to start coding and automating your tasks
Default language is ImageJ macro

## Slide 23: Writing Code in ImageJ
End a command with ;
Write comments using // to “comment-out” so it’s not read as code
  Annotate your code so you and others understand it
  It might make sense when you write it, but no 6 months later!
Data types:
  String
    “Anything in quotation marks. Even numbers! 01234……”
  Number
    No quotation marks. These are recognised as numbers and you can do maths
  Array
    A list of numbers or strings (or both – this can get confusing though so try to avoid)
Variables:
  Arbitrary names you can give to things to recall them later e.g.
  Name=“James”;
  print(Name);
  “James”

## Slide 24: Modifying Strings
Add variables to strings
  Name=“James”;
  print(“My name is ”+Name);
  My name is James
Common operation in Fiji, to modify commands e.g.
Img_1=“Image_1_filename.tiff”;
Img_2=“Image_2_filename.tiff”;
open("C:/Desktop/“+Img_1);
open("C:/Desktop/“+Img_2);

## Slide 25: Exercise 3

## Slide 26: Adding plugins
Help > Update > Manage update sites
Select:
  CSB Deep
  Stardist
  SCF MPI CBG
  IJPB-plugins
Apply changes
Restart Fiji

## Slide 27: Quantification in images

## Slide 28: Background subtraction
Background signal will exist in images
  May vary within individual images
  Will vary between images
This background will influence the values recorded for your real signal
Can try to remove background to normalise intensity values
2 main methods to correct
  Manual subtraction: measure the background e.g. average signal over an area, and subtract from the total image signal
  “Background subtraction” function: calculates average background in a “rolling ball” and subtracts them.
    Particularly useful for uneven background
Keep any correction technique consistent
NB. Macros enable you to document how work was done, as well as repeating it.
Original (118x118)
Subtracted 19
Rolling ball (40px)

## Slide 29: Plot profile (Ctrl+K)

## Slide 30: “Measure”
The values calculated by the Measure function can be specified separately in Set Measurements
Can also specify measurements to be taken from another image e.g. a different channel

## Slide 31: Image Segmentation
For counting objects and measuring relationships between them we need to segment
Achieved by thresholding
Classification of pixels as either:
  0 - Not what you’re interested in
  1 - The thing you’re interested in (255 in 8bit)
  This is a binary classification and can be shown as a binary mask
Original
Thresholding
Binary Mask

## Slide 32: Thresholding
Manual
  Signal within a range you specify
Automatic
  Range specified by an algorithm
  Lots of options (see what works for you)
  Otsu particularly popular

## Slide 33: Noise
Images captured always feature some degree of noise from the camera
Other small unwanted features also commonly exist in microscopical images
This signal can impair the ability to segment images
Noisy Image
Auto-Segment: Otsu

## Slide 34: Filtering
Filters can help remove noise (and have other uses)
Pass a window over the image, mathematically processing pixel values dependent on neighbouring values
Gaussian filter commonly used
  Weighted filter smooths signal
Read more here:
  https://bioimagebook.github.io/chapters/2-processing/4-filters/filters.html
Noisy Image
Auto-Segment: Otsu
Gaussian Filter

## Slide 35: Binary Operations

## Slide 36: Binary Operations
Dilation + Erosion can make edges more uniform
Erosion + Dilation can separate objects

## Slide 37: Watershedding

## Slide 38: Watershedding
Separate adjacent objects
Consider the image intensities as an inverted mountain range
  Furthest points from the edge are the valley bottoms
  Where would the pools join if filled with water?
There are several variations on this

## Slide 39: Labelmaps
Images can be used to represent regions classified by segmentation
Values no longer reflect the signal intensity, but rather a classification
Binary images (0/1 i.e. yes/no)
Labelmaps (a range of unique integers)
  Each number is a unique ID for each segmented object

## Slide 40: Measure binary objects with “Analyze Particles”
Now that your image contents have been segregated, their features can be measured

## Slide 41: Page 4

## Slide 42: Machine Learning
Install CSB Deep and Stardist in ImageJ Updates
Pretrained neural network
Works very well with to segment round objects (nuclei, round cells)

## Slide 44: Page 4b

## Slide 45: Arrays
files=newArray("File_1","File_2","File_3");
Array.show(files);//displays array
Arrays contain a list of values
These can be numbers, strings or both

## Slide 46: Arrays to tables
String_Array=newArray("File_1","File_2","File_3");
Number_Array=newArray(1,2,3);
Mixed_Array=newArray(100,5,"Rubbish_Image");
//Combine to make a table
Table.showArrays("Lovely_Table", String_Array, Number_Array, Mixed_Array);
Really useful for outputting bespoke data

## Slide 47: Loops
Looping is extremely useful for processing batches of data
Loops iteratively move through arrays e.g.
  Batches of images in a folder
  Lists of values for mathematical analysis
Initialise
Code block
Last Iteration?
End
NO
YES

## Slide 48: Loops in Fiji
for (i = 0; i < 10; i++) {
print(i);
}
Initialise loop:
i is an arbitrary name for a variable
i=0 is the starting value (“initialization”)
i<10 keep going while value of i is <10 (“condition”)
i++ add one (“increment”)
Code block:
Contained between {}

## Slide 49: Conditional Statements (if/else)
Yes/No expression (“Boolean”)
Question
Code block
End
NO
YES

## Slide 50: Conditional Statements (if/else)
Question
Code block
End
NO
YES
Different
Code block

## Slide 51: Conditional Statements (if/else)
x=2;
if(x>1){
print("x is bigger than one");
}
else{
print("x is not bigger than one");
}

## Slide 52: Dialogues
Popups for manual intervention

## Slide 53: Page 5

## Slide 54
“Imaging Forum”
  Building a bioimaging community at UoE
  Technical and research seminars
  Discussion and skill sharing
  Email me to be added (j.c.crichton@exeter.ac.uk)